Active localization
Plans for a few demos

---
Many-door example*
- Objective
  - Testing accuracy of algorithms
  - Bayes filtering results as ground truth
*inspired by the three-door problem in Probabilistic Robotics

---
Many-door example
- Map1
  - Doors distributed on a finite section of real line
D-
D+
D1
0
D+ = 1000 cm
D- = -1000 cm
D1 = 500 cm

---
- Measurement model
  - A range finder detecting its distance to the closest door.
z
D
x
Z = abs(x-D)
*temporarily we assume zmax is infinite

---
- Process model
  - The robot can move with a constant speed
    - 100 cm/s
*temporarily we assume zmax is infinite

---
- Approaches
  - Bayes filter
  - Greedy technique
  - Candidates are within [-2000, -1900,…,1900, 2000] initially
2δ